## Slide 1: Edge Intelligence
17. May 2022
Dr. Gibson Kimutai

## Slide 2: Objectives
Learn how to plan a complete network
Learn how to evaluate and compare different network architectures
Learn how to distribute the intelligence
Practice on some examples

## Slide 3: Network Intelligence Planning
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface
Example 1: Potato field irrigation system
  Sense temperature and soil moisture in a flat field, irrigate automatically
  Field is approximately 1 hectare, with approx. 20 measurement and irrigation points
  Situated in urban Germany, 4 G is available. Power supply is available at one place (water pump)
Example 2: Elephant recognition with underground vibration
  Burry vibration sensors between a village in Sri Lanka and the nearby forest.
  Once an elephant I recognized, notify users.
  4G is not available (neither anything else)

## Slide 4: Sensors / Applications
What kind of sensors?
How often to read them out?
How much power?
How much data do they produce?
Do we have actuators? How to trigger them?
How many sensors?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 5: Sensors / Applications : Example 1
Soil temperature, volumetric water content
Read them out every morning and every evening
3.3V - 5V, depending on manufacturer
Tens of bytes
Irrigation valve (5V); triggered when VWC below X% and temperature above Y° (a table) and the weather forecast has rain probability for the next 6 hours of below 80% and it is not currently raining.
Approx. 20 sensors, spread over 1 hectare.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 6: Intelligence
Design the complete network (all steps of the following process) on paper for the following options:
  Option 1: Put the complete intelligence to the cloud (edge-cloud continuum). Sensors only push data to the cloud. Actuators and events are controlled by the cloud.
  Option 2: Put the complete intelligence to the edge. Edge sensors are completely independent of each other and can do everything alone. Cloud can be omitted completely or used only for backup of data.
Evaluate and discuss the pros and cons of the extreme options. Distribute the intelligence between edge, fog and cloud to meet your requirements and to optimize costs (resources, internet connection, human intervention, number of devices, etc.)
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 7: Intelligence : Example 1
Option 1, cloud based: Measure the data, push the data to the cloud, wait for a command from the cloud to activate the irrigation valves.
Option 2, edge based: Measure the data, evaluate the data and take into account the weather forecast, decide whether to irrigate or not.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 8: Edge device
How much memory and CPU needed?
Which other components needed (clock, external memory, voltage regulators, etc.)?
How large?
How to protect?
How to power supply?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 9: Edge device, Example 1, Cloud
Very low requirements, any microcontroller would do.
One or two additional rain sensors would be needed. Alternative: receive rain data from cloud (not local enough?)
Clock is needed to trigger the measurements (alternative: wake up every x seconds and wait for polling from cloud). No external memory. Voltage regulators needed (more reliable).
Small device in a small waterproof box, with waterproof connections to irrigation valve.
Waterproof, protect from direct sunlight.
Battery would be enough (measuring only twice a day and then waiting for commands to come), assuming the irrigation pump has its own power supply.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 10: Edge device, Example 1, Edge
Simple measurements and analysis (comparisons only), a ”larger” microcontroller would do.
One or two additional rain sensors would be needed. Alternative: receive rain data from cloud (not local enough?)
Clock is needed; No external memory if cloud is used for backup (more convenient in case of errors and for monitoring). Voltage regulators needed (more reliable).
Small device in a small waterproof box, with waterproof connections to irrigation valve.
Waterproof, protect from direct sunlight.
Battery would be enough (measuring only twice a day and then waiting for commands to come) , assuming the irrigation pump has its own power supply.
Connection to cloud needed for receiving weather forecasts!
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 11: Wireless
Who needs to communicate to whom? How much data and how often?
What is available already? 4G? WiFi? LoRa? SigFox?
Can we install gateways (power supply, legal issues, etc.)?
What is the price of the available options?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 12: Wireless : Example 1, Cloud
Edge devices need to communicate to cloud and back.
Edge devices need to exchange rain data. Alternative: get it from the cloud.
Data is small, exchange only in the morning/evening.
4G is available. 1 Gateway can be installed (e.g. at the water pump).
Options:
  4G – very expensive, needs a SIM card at each device.
  NB-IoT – needs a SIM card, lower price than 4G. Good option.
  WiFi – very short transmission radius, will need lots of gateways.
  LoRa – transmission radius needs to be tested (will 1 gateway be enough?); can implement also a multi-hop transmission to gateway. Good option.
  ZigBee – will be similar to LoRa, but has built-in support for multihop. Good option.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 13: Wireless : Example 1, Edge
Edge devices need to communicate to cloud (backup) and back (forecasts).
Edge devices need to exchange rain data. Alternative: get it from the cloud.
Data is small, exchange only in the morning/evening or even less.
4G is available. 1 Gateway can be installed (e.g. at the water pump).
Options:
  4G – very expensive, needs a SIM card at each device.
  NB-IoT – needs a SIM card, lower price than 4G. Good option.
  WiFi – very short transmission radius, will need lots of gateways.
  LoRa – transmission radius needs to be tested (will 1 gateway be enough?); can implement also a multi-hop transmission to gateway. Good option.
  ZigBee – will be similar to LoRa, but has built-in support for multihop. Good option.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 14: Gateways
How many? Where to place? Power supply?
Can they cater for some intelligence or data caching?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 15: Gateways : Example 1, Cloud
Need to make an experiment for transmission radius with LoRa, NB-IoT and Zigbee.
  Results very positive (single gateway works): go for LoRa or Zigbee.
  Results not positive (more gateways needed): compute exact costs for NB-IoT and compare to LoRa or ZigBee multihop.
Can they cater for some intelligence or data caching?
  They could cache the forecasts and the irrigation commands. This would make the solution with LoRa or Zigbee much easier (devices can poll the information from the gateway)
  They can also cache the rain data, so that no device-to-device communication is needed.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 16: Gateways : Example 1, Edge
Need to make an experiment for transmission radius with LoRa, NB-IoT and Zigbee.
  Results very positive (single gateway works): go for LoRa or Zigbee.
  Results not positive (more gateways needed): compute exact costs for NB-IoT and compare to LoRa or ZigBee multihop.
Can they cater for some intelligence or data caching?
  They could cache the forecasts and the irrigation commands. This would make the solution with LoRa or Zigbee much easier (devices can poll the information from the gateway)
  They can also cache the rain data, so that no device-to-device communication is needed.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 17: Cloud
What kind of data will be stored, for how long and how much?
Costs, availability, privacy and security requirements
Do we offer user services directly from the cloud?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 18: Cloud : Example 1, Cloud
All sensor data will be stored for the complete time of the project (several years), not a large amount in total (GB).
Costs, availability, privacy and security requirements:
  Costs as low as possible (open source, free)
  Availability is not critical (if data is lost, not a big problem)
  Privacy and security important, since actuators are controlled.
Do we offer user services directly from the cloud?
  Control the irrigation valves
  Data analysis
  A smartphone app to see the last couple of days the data and when the irrigation valves were active; how much water was consumed.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 19: Cloud : Example 1, Edge
All sensor data will be stored for the complete time of the project (several years), not a large amount in total (GB).
Costs, availability, privacy and security requirements:
  Costs as low as possible (open source, free)
  Availability is not critical (if data is lost, not a big problem)
  Privacy and security not critical, as only backup.
Do we offer user services directly from the cloud?
  Data analysis
  A smartphone app to see the last couple of days the data and when the irrigation valves were active; how much water was consumed.
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 20: Summary of Example 1
Difference between edge and cloud alternatives minimal
Need to decide how to measure rain
Need to do wireless experiments
Need to calculate prices of NB-IoT, LoRa and Zigbee
Possible decision 1:
  Use local rain sensors, let the devices send it to the gateway.
  Use LoRa (less expensive, practical experience).
  Store forecasts in the gateway.
  Put the intelligence on the edge (more independent from cloud and its reliability, from wireless problems)
Possible decision 2:
  Put the intelligence on the cloud
  Use LoRa
  Do not use rain sensors, trust the weather information on the cloud (e.g. a local weather station available).

## Slide 21: Summary
A creative process, depends a lot on experience
Compare the two extreme options, mixed options typically emerge from alone
Do not scared of new technologies, but evaluate them carefully before usage (e.g. in our example: Zigbee or NB-IoT).

## Slide 22: Network Intelligence Planning
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface
Example 1: Potato field irrigation system
  Sense temperature and soil moisture in a flat field, irrigate automatically
  Field is approximately 1 hectare, with approx. 20 measurement and irrigation points
  Situated in urban Germany, 4 G is available. Power supply is available at one place (water pump)
Example 2: Elephant recognition with underground vibration
  Burry vibration sensors between a village in Sri Lanka and the nearby forest.
  Once an elephant I recognized, notify users
  4G is not available (neither anything else)

## Slide 23: Sensors / Applications: Example 2
What kind of sensors?
How often to read them out?
How much power?
How much data do they produce?
Do we have actuators? How to trigger them?
How many sensors?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 24: Intelligence: Example 2
Design the complete network (all steps of the following process) on paper for the following options:
  Option 1: Put the complete intelligence to the cloud (edge-cloud continuum). Sensors only push data to the cloud. Actuators and events are controlled by the cloud.
  Option 2: Put the complete intelligence to the edge. Edge sensors are completely independent of each other and can do everything alone. Cloud can be omitted completely or used only for backup of data.
Evaluate and discuss the pros and cons of the extreme options. Distribute the intelligence between edge, fog and cloud to meet your requirements and to optimize costs (resources, internet connection, human intervention, number of devices, etc.)
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 25: Edge device: Example 2
How much memory and CPU needed?
Which other components needed (clock, external memory, voltage regulators, etc.)?
How large?
How to protect?
How to power supply?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 26: Wireless: Example 2
Who needs to communicate to whom? How much data and how often?
What is available already? 4G? WiFi? LoRa? SigFox?
Can we install gateways (power supply, legal issues, etc.)?
What is the price of the available options?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 27: Gateways: Example 2
How many? Where to place? Power supply?
Can they cater for some intelligence or data caching?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 28: Cloud: Example 2
What kind of data will be stored, for how long and how much?
Costs, availability, privacy and security requirements
Do we offer user services directly from the cloud?
Sensors / Application
Where is the intelligence?
Wireless technology
Edge device
Gateways / Fog
Cloud Services / User Interface

## Slide 29: Example 2: Actions and Open Questions